‘S’ Type Combination Unit 2022

Delivery only for DIY

# Timber sizes nominal before planning and processing, other dimensions may vary dependant on individual building.

| Unit Size | Shelter Size | Store Size | Height | Height | Price |
| --- | --- | --- | --- | --- | --- |
| (widthxdepth) | (widthxdepth) | (widthxdepth) | (at front) | (at rear) | (Ex VAT) |
| 4.2 x 2.4m | 3.0 x 2.4m | 1.2 x 2.4m | 2.05m | 1.75m | £1,585.00 |
| 4.2 x 1.8m | 3.0 x 1.8m | 1.2 x 1.8m | 1.57m | 1.40m | £1,295.00 |

General Specifications:

Front roof Height: 		2050mm excluding skid

Rear roof Height:		1750mm excluding skid

Overhang:			Nil

Skid:				80x40mm galvanised skid with

galvanised towing points

Framework:	Constructed from 75x50mm cls

tanalith E treated timber at 600mm centres.

Studwork doubles at door apertures.

Cladding:	Premium ex19mm tanalith E treated

overlap shiplap

Purlins:		100x50mm positioned at a maximum of

600mm centres

Roofing:	Black Onduline with Onduline ridge capping

lined with 11mm OSB

Guttering:		Nil

Shelter Section:

Opening Size: 		1.8m (w)

Kickboarding:		Lined to 1.22m with 11mm OSB

Store Section:

Opening Size: 		810mm includes tack door

Roof:				Boarded with 11mm OSB underneath

Onduline

Floor:				100x50mm bearers at max 600mm

Centres 18mm flooring

Walls:				Unlined internally, except diving wall

Which is lined to roofline

# Text boxes

Tel: 01403 785508

Email: enquiries@redmire.co.uk